## Slide 1
The Lego® Spectrophotometer
Practical Investigations of Dye
December 2022
Notes: Play the CTL lab video (with subtitles) as students are coming in. Link: https://www.youtube.com/watch?v=0WrD-cC348k
Link from CTL:
That was one of our third years saying that what makes Oxford for her is working with some of the best researchers in the world. And we’re going to focus on one of nearly 90 world-class research groups at Oxford during our workshop today, Plastics from Another Perspective
Start screen.

## Slide 2
Workshop objectives:
To build a Lego® Spectrophotometer
To gain an understanding of how spectrophotometers work.
To apply simple circuitry to build a functional spectrophotometer.
To measure the rate constant for the reaction between the dye and bleach using a logarithmic plot

## Slide 3
What is Spectrophotometry?
Spectrophotometry is a type of electromagnetic spectroscopy which allows determination of the absorptivity or transmittivity of a substance under investigation. Spectrophotometry is commonly used in:

## Slide 4
How Do Spectrophotometers Work?
1. Polychromatic light source.
2. Monochromator refocuses only one wavelength onto the cuvette.
3. Focussed light passes through the sample with incident intensity, I0. Sample absorbs some light and transmits the rest, with transmission intensity, I. Since some light is absorbed by the sample, I0 > I.
4. Light with transmitted intensity, I, reaches the detector which displays an output of voltage.
5.The resultant voltage can be used to deduce the transmitted intensity. Voltage, V, is directly proportional to transmitted intensity, I.

## Slide 5
Why are objects coloured?
Notes: Most objects will absorb some wavelengths of light better than others and the colour of a substance depends on the wavelengths of light that it absorbs. For a solution to appear as a particular colour, the dissolved compound must absorb the complementary colour to which it appears. Complementary colours lie opposite on a colour wheel.
The interaction of light with the sample is an important consideration in the Lego® spectrophotometer. We must choose a light source that the compound will absorb in order to record accurate optical measurements. To investigate different coloured dyes you need to choose a correctly coloured LED light source. In the case of Brilliant Blue FCF, which appears blue, what colour light is needed?
A: Orange – it is opposite blue on the colour wheel.

## Slide 6
Why do dye molecules absorb light?
Highest occupied molecular orbital
(HOMO)
Lowest unoccupied molecular orbital
(LUMO)
Notes: Electrons in compounds can be excited from the HOMO (highest occupied molecular orbital) to the LUMO (lowest unoccupied molecular orbital) by absorbing energy in the form of a photon (see Figure 4). In the case of many conjugated systems, the photon (packet of energy) absorbed to excite an electron lies in the visible light region, and so the compound appears coloured. The wavelength of the absorbed photon will correspond to the complementary colour of the compound.

## Slide 7
Beer-Lambert Law
The Beer Law states that:
Where
A = sample absorbance
= concentration (normally in mol dm-3),
= path length (1 cm for standard cuvettes)
e = absorption coefficient (normally in mol-1 dm3 cm-1).

## Slide 8
Kinetics of Brilliant Blue FCF bleaching
In this practical, you will determine the rate law for the reaction of Brilliant Blue FCF dye and bleach.

## Slide 9
Background
Dye Oxidation
blue
colourless
Notes: Bleach is a strong oxidising reagent. Brilliant Blue FCF is highly susceptible to oxidation by bleach because the products are quite stable due to their reasonable levels of conjugation. The oxidised products are colourless, because the extended -conjugation of the dye is lost upon oxidation, which results in an increased HOMO-LUMO energy gap. The photon energy absorbed is in the UV range, so the products appear colourless.
The rate of a reaction is usually expressed in terms of how the concentration of either the products or one of the reactants changes over time.
In this case, since the dye reactant is strongly coloured and the products are colourless, it is convenient to track the concentration of dye during the reaction.
Bleach is a strong oxidising reagent. Brilliant Blue FCF is highly susceptible to oxidation by bleach because the products are quite stable due to their reasonable levels of conjugation. The oxidised products are colourless, because the extended 𝜋-conjugation of the dye is lost upon oxidation, which results in an increased HOMO-LUMO energy gap. The photon energy absorbed is in the UV range, so the products appear colourless.
The rate of a reaction is usually expressed in terms of how the concentration of either the products or one of the reactants changes over time.
In this case, since the dye reactant is strongly coloured and the products are colourless, it is convenient to track the concentration of dye during the reaction.

## Slide 10
and will be determined in the following experiments.
For now, let’s consider this reaction where bleach is in huge excess, and [bleach] is constant:
Dye Product
Where
Notes: To determine the order of a reactant in a reaction, we need to calculate how the concentrations of the reactants change over time as the reaction happens. It is normally easier to start with one reagent in excess. In this case, the bleach is in a very large excess, meaning the concentration of bleach is almost constant over time, and the rate law can be simplified to:

## Slide 11
A Zeroth order reaction is one in which m = 0. A general rate equation for a zeroth order reaction is:
We can integrate this equation (you don’t need to know how) to get the integrated rate law:
Zeroth Order
Notes: What would we plot to find k’?

## Slide 12
A reaction where m = 1 is called a first order reaction. The rate law for this reaction is:
The integrated form of this rate law is:
First Order
Notes: What would we plot to find k’?

## Slide 13
A reaction where m = 2 is called a second order reaction. The rate law for this reaction is:
The integrated form of this rate law is:
Second Order
Notes: What would we plot to find k’?

## Slide 14
Half Lives
[dye] = [dye]0/2
Notes: Half-life, t1/2, is defined as the time taken for the initial concentration of a particular reactant to halve.
The relationship between [dye]0 and t1/2 can be determined from the integrated rate laws above. This is done by solving the equation for t when [dye] = [dye]0/2

## Slide 15
Build the Lego® Spectrophotometer
Important!
1. Always use the resistor.
2. Before anything else: make sure LEDs are working and check which colour is which.
3. Once built, move immediately to the experimental stage.
For the experiment, make sure to:
Read all the instructions first, particularly steps 4 & 5.
Set voltmeter to 200m (V).
Start the
Experiment

## Slide 16
Any questions

## Slide 17
Find out more about the work of the Department of Chemistry at
www.chem.ox.ac.uk
outreach@chem.ox.ac.uk
@ChemOutreachOxf
vector created by starline